Bits & Bots

---
Bits & Bots Sessions
Bits & Bots Sessions
Session	Topic
Tuesday 20th May, 6 – 8pm	Intro to 3D Design: Design custom robot parts to print on the 3D printers
Tuesday 27th May, 6 – 8pm	Intro to Electronics: Learn how the electronic parts in the kit work, design our robot circuits
Tuesday 3rd Jun,e 6 – 8 pm	Intro to Arduino: Write NodeJS programs to read from sensors and control actuators
7th June, 1 – 5 pm	Intermediate 3D Design: Design more complex robot parts: gears, claws etc
14th June, 1 – 5 pm	Intermediate Arduino: Develop our robots' locomotion, sensing and responding behaviours
21st June, 1 – 6 pm	Advanced Bits & Bots: Finalise robot design and assembly, develop advanced robot control programs

---
Bits & Bots Slides etc
Bits & Bots Slides etc
Slides and other materials for the course will be published after each session here:
https://github.com/AnnaGerber/bits-n-bots

---
Chassis
Sensors
(Inputs e.g. ultrasonic sensor)
Power
Control
(Microcontroller = brain)
Actuators
(Outputs e.g. motors)

---
Physical Computing
Physical Computing
Building interactive systems that sense and act on (or respond to) the physical world

---
Electricity
Electricity
- Electricity is a form of energy
- We can connect components that convert electrical energy into other forms of energy: light, sound, movement, heat etc, into a circuit
- In a Direct Current (DC) circuit,
  electrical energy flows from
  the positive side of a
  power source to the
  negative side, i.e. from
  + (power) to – (ground)

---
Electrical concepts
Electrical concepts
- Current (Amps): measures the flow of electrical energy through a circuit
- Voltage (Volts): measures difference in potential energy between the positive and negative sides of a circuit
- Resistance (Ohms): measures a material's opposition to the flow of energy
- Power (Watts): the rate at which energy is converted from one form to another

---
Ohm's Law
Ohm's Law
Current = Voltage / Resistance
- Increase the voltage, and the current will increase (i.e. speed up)
- Increase the resistance and the current will decrease

---
Circuit Schematics
Circuit Schematics
Diagrammatic representations of components and how they are connected

---
Using a Breadboard
Using a Breadboard
- Use to prototype circuits without soldering by plugging in components and jumper wires
- Numbered rows are connected
- Some have power rails along the sides

---
Resistors
Resistors
- Introduces resistance, so restricts the amount of current that can flow through a circuit
- Can be connected in either direction
- Bend and trim the leads to approx 1cm each make it easier to use with the breadboard

---
LEDs
LEDs
- Light Emitting Diode
- Polarized: diodes act like one way valves so must be connected in a certain direction
- Emits light when a current passes through
Cathode (-)
connects to ground
Anode (+)
longer lead
connects to power

---
Creating a circuit
Creating a circuit
- Hook up an LED to a power source: anode to + and cathode to -
- Include a current limiting resistor to avoid damaging the LED

---
Adding more components
Adding more components
Add a second LED to your circuit, experiment with connecting the LEDs in parallel vs series

---
Pushbuttons
Pushbuttons
- Also known as a momentary switch
- Can be connected in either direction
- Has two sets of leads on either side
Use leads from the same side together

---
Add a button to your circuit
Add a button to your circuit

---
Control
Control
- Microcontroller co-ordinates robot inputs (sensors) and outputs (actuators)
- We are using an Arduino Nano clone
- See http://arduino.cc/

---
Sensors
Sensors
- Environmental conditions   (e.g. temperature, humidity, smoke)
- Magnetic (e.g. hall effect sensor)
- Light (e.g. photo resistor)
- Sound (e.g. microphone)
- Motion (e.g. accelerometer, tilt, pressure)
- User / Physical Input (e.g. button)

---
Sensors in our kits
Sensors in our kits
PHOTO RESISTOR / Produces a variable resistance dependant on the amount of incident light.
Ultrasonic Sensor / Used to detect distance from objects.
PUSHBUTTON / Can be used as a bump sensor: indicates that the robot has bumped into something when pressed

---
Actuators
Actuators
- Light & Displays (e.g. LED, LCD)
- Sound (e.g. Piezo buzzer)
- Motion (e.g. Servo, DC Motor, Solenoid)
- Power (e.g. Relay)

---
Actuators in our kits: Light and Sound
Actuators in our kits: Light a Sound
PIEZO ELEMENT / A pulse of current will cause it to click. A stream of pulses will cause it to emit a tone.
LED & RGB LED / We are using Common Cathode RGB LEDs. The longer lead is the common lead which connects to ground. The three other leads are for Red, Green and Blue signal
LED Matrix / 8 x 8 matrix of single colour LEDs. One row 8 pins corresponds to rows and the other to columns. We will connect to these pins via shift registers.

---
Actutators in our kit: Motors
Actuators in our kit: Motors
9g Hobby Servo / A box containing a motor with gears to make it positionable from 0 to 180 degrees. Positioning is controlled through a timed pulse, between 1.25 milliseconds (0 degrees) and 1.75 milliseconds (180 degrees) (1.5 milliseconds for 90 degrees).
Continuous Rotation Servo / A servo that rotates 360 degrees

---
Digital vs Analog
Digital vs Analog
Digital
  - discrete values (0 or 1)
  - Examples: tilt sensor, push button
- Analog
  - continuous values
  - typically values for analog sensors are constrained within a range e.g. 0 – 255, 0 – 1023
  - Example: photo resistor
- Some sensors and actuators support both digital and analog modes

---
Connecting a servo
Connecting a servo
- Connect the red lead to power
- Connect the brown (sometimes black) lead to ground
- Connect the orange (sometimes yellow) signal lead to one of the I/O pins on the Arduino that supports Pulse Width
  Modulation (PWM):
  3, 5, 6, 9, 10, 11

---
Connecting a sensor
Connecting a sensor
- Connect VCC to power
- Connect GND to ground
- Connect the other pin(s) to I/O pins on the Arduino

---
Credits
Credits
- Some of the images in these slides were taken from the Arduino Experimenters Guide created by .:oomlout:. and SparkFun and are used under a CC-BY-SA license.
- See http://node-ardx.org for more details